## Slide 1: CS/ECE 552: Midterm Review
Lecture notes based in part on slides created by Matt Sinclair, Mikko Lipasti, Mark Hill, Josh San Miguel, and John Shen

## Slide 2: Key Ideas
Iron Law
Amdahl's Law
MIPS ISA – R, I, J type instructions
Single Cycle Instruction Data and Control Path
Pipelining
Data and Control Hazards
Forwarding/Bypassing Examples
Superscalar, VLIW, Out of Order – Why we need it, What does it enable

## Slide 3: Register File Bypassing
Producer instruction:
Writes into a register
Consumer instruction:
Reads that register
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $t0, $t1, $t2 | F | D | X | M | W |  |  | 
… |  | F | D | X | M | W |  | 
… |  |  | F | D | X | M | W | 
add $s0, $s0, $t0 |  |  |  | F | D | X | M | W
3
COD Figure 4.65

## Slide 4: EX-to-EX Forwarding
Producer instruction:
Writes an ALU result into a
register
Consumer instruction:
Reads that register and needs its value for ALU
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $t0, $t1, $t2 | F | D | X | M | W |  |  | 
add $s0, $s0, $t0 |  | F | D | X | M | W |  | 
4
COD Figure 4.65

## Slide 5: MEM-to-EX Forwarding
Producer instruction:
Writes an ALU result into a
register
Consumer instruction:
Reads that register and needs its value for ALU, one cycle later
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $t0, $t1, $t2 | F | D | X | M | W |  |  | 
… |  | F | D | X | M | W |  | 
add $s0, $s0, $t0 |  |  | F | D | X | M | W | 
5
COD Figure 4.65

## Slide 6: MEM-to-EX Forwarding
Producer instruction:
Writes a loaded memory
result into a register
Consumer instruction:
Reads that register and needs its value for ALU
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
lw $t0, 0($t1) | F | D | X | M | W |  |  | 
sw $s0, 0($t0) |  | F | D* | D | X | M | W | 
6
COD Figure 4.65

## Slide 7: MEM-to-MEM Forwarding
Producer instruction:
Writes a loaded memory
result into a register
Consumer instruction:
Reads that register and needs its value for storing to memory
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
lw $t0, 0($t1) | F | D | X | M | W |  |  | 
sw $t0, 0($s0) |  | F | D | X | M | W |  | 
7
COD Figure 4.65

## Slide 8: EX Forwarding to Branch in ID
Producer instruction:
Writes an ALU result into a
register
Consumer instruction:
Reads that register and needs its value for branch decision in ID
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
add $t0, $t1, $t2 | F | D | X | M | W |  |  | 
beq $s0, $t0, DST |  | F | D* | D | X | M | W | 
8
COD Figure 4.65

## Slide 9: Register File Bypassing to Branch in ID
Producer instruction:
Writes a loaded memory
result into a register
Consumer instruction:
Reads that register and needs its value for branch decision in ID
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
lw $t0, 0($t1) | F | D | X | M | W |  |  | 
beq $s0, $t0, DST |  | F | D* | D* | D | X | M | W
9
COD Figure 4.65

## Slide 10: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.

## Slide 11: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 

## Slide 12: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D |  |  |  |  |  |  |  |  | 

## Slide 13: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 

## Slide 14: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F |  |  |  |  |  |  |  |  | 

## Slide 15: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D |  |  |  |  |  |  | 

## Slide 16: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 

## Slide 17: Data Forwarding
lw $t0, 0($t1)
lw $s1, 4($t0) add $t2, $t3, $s1
At which cycle(s) is this forwarding path enabled?
Assume full forwarding and bypassing.
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
lw $t0 | F | D | X | M | W |  |  |  |  |  |  |  | 
lw $s1 |  | F | D* | D | X | M | W |  |  |  |  |  | 
add |  |  | F* | F | D* | D | X | M | W |  |  |  | 
Therefore, cycle 4 and 7.

## Slide 18: Practice Problem-1

## Slide 19: Five-Stage Pipeline
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP

## Slide 20: Five-Stage Pipeline: Q1
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
no control hazard flushes!

## Slide 21
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI = 1?
Five-Stage Pipeline: Q1

## Slide 22: Five-Stage Pipeline: Q1
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI = 1 + (2) / 5?
RAW, 2-cycle stall

## Slide 23: Five-Stage Pipeline: Q1
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI = 1 + (2) / 5?
RAW, 2-cycle stall
RAW, no need to stall

## Slide 24: Five-Stage Pipeline: Q1
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI = 1 + (2 + 1) / 5?
RAW, 2-cycle stall
RAW, 1-cycle stall

## Slide 25: Five-Stage Pipeline: Q1
Assume RF bypassing but no forwarding. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI = 1 + (2 + 1) / 5 = 1.6
RAW, 2-cycle stall
RAW, 1-cycle stall

## Slide 26: Five-Stage Pipeline Q2
Assume forwarding and bypassing except MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI0 = 1 + (2 + 1) / 5 = 1.6
RAW, 2-cycle stall
RAW, 1-cycle stall

## Slide 27: Five-Stage Pipeline Q2
Assume forwarding and bypassing except MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI0 = 1 + (2 + 1) / 5 = 1.6
CPI1 = 1 + (2) / 5
RAW, 2-cycle stall
RAW, 1-cycle stall

## Slide 28: Five-Stage Pipeline Q2
Assume forwarding and bypassing except MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
CPI0 = 1 + (2 + 1) / 5 = 1.6
RAW, 1-cycle stall
CPI1 = 1 + (1) / 5
27

## Slide 29: Five-Stage Pipeline Q2
Assume forwarding and bypassing except MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
RAW, 1-cycle stall
CPI0 = 1 + (2 + 1) / 5 = 1.6
CPI1 = 1 + (1) / 5 = 1.2

## Slide 30: Five-Stage Pipeline Q2
Assume forwarding and bypassing with MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP
RAW, 1-cycle stall
CPI0 = 1 + (2 + 1) / 5 = 1.6
CPI1 = 1 + (1) / 5 = 1.2

## Slide 31: Five-Stage Pipeline Q3
CPI0
CPI1 CPI2
= 1 + (2 + 1) / 5 = 1.6
= 1 + (1) / 5 = 1.2
= 1
Assume forwarding and bypassing with MEM-to-MEM. Assume all control hazards are perfectly predicted and that you never have to flush. Consider this long-running loop, what is the average CPI?
LOOP:
lw $s0, 0($s1) sw $s0, 4($s1) add $t0, $t0, $s0 addi $s1, $s1, 8
bne $s0, $zero, LOOP

## Slide 32: Practice Problem-2

## Slide 33: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
lw $s0, 0($s0) sw $s0, 0($t0)
bne $s0, $zero, SKIP
lw $t1, 4($s0) sw $s1, 0($t1)
# taken
SKIP:

## Slide 34: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
sw $s0, 0($t0) |  | F | D | X | M | W |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
lw $s0, 0($s0) sw $s0, 0($t0)
bne $s0, $zero, SKIP
lw $t1, 4($s0) sw $s1, 0($t1)
# taken
SKIP:

## Slide 35: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
sw $s0, 0($t0) |  | F | D | X | M | W |  |  |  |  |  |  |  | 
bne $s0, $zero, SKIP |  |  | F | D* | D | X | M | W |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
lw $s0, 0($s0) sw $s0, 0($t0)
bne $s0, $zero, SKIP
lw $t1, 4($s0) sw $s1, 0($t1)
# taken
SKIP:

## Slide 36: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
sw $s0, 0($t0) |  | F | D | X | M | W |  |  |  |  |  |  |  | 
bne $s0, $zero, SKIP |  |  | F | D* | D | X | M | W |  |  |  |  |  | 
lw $t1, 4($s0) |  |  |  | F* | F | = |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
lw $s0, 0($s0) sw $s0, 0($t0)
bne $s0, $zero, SKIP
lw $t1, 4($s0) sw $s1, 0($t1)
# taken
SKIP:

## Slide 37: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  | 
sw $s0, 0($t0) |  | F | D | X | M | W |  |  |  |  |  |  |  | 
bne $s0, $zero, SKIP |  |  | F | D* | D | X | M | W |  |  |  |  |  | 
lw $t1, 4($s0) |  |  |  | F* | F | = |  |  |  |  |  |  |  | 
sw $s1, 0($t1) |  |  |  |  |  | F | D | X | M | W |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
lw $s0, 0($s0) sw $s0, 0($t0)
bne $s0, $zero, SKIP
lw $t1, 4($s0) sw $s1, 0($t1)
# taken
SKIP:

## Slide 38: Practice Problem-3

## Slide 39: Pipeline Diagrams
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 40: Pipeline Diagrams
5
6
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 41: Pipeline Diagrams
5
7
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 42: Pipeline Diagrams
5
8
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
lw $t0, 4($s0) |  |  | F* | F* | F | = |  |  |  |  |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 43: Pipeline Diagrams
5
9
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
lw $t0, 4($s0) |  |  | F* | F* | F | = |  |  |  |  |  |  |  |  |  | 
lw $s0, 0($s0) |  |  |  |  |  | F | D | X | M | W |  |  |  |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 44: Pipeline Diagrams
6
0
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
lw $t0, 4($s0) |  |  | F* | F* | F | = |  |  |  |  |  |  |  |  |  | 
lw $s0, 0($s0) |  |  |  |  |  | F | D | X | M | W |  |  |  |  |  | 
bne $s0, $zero, LOOP |  |  |  |  |  |  | F | D* | D* | D | X | M | W |  |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 45: Pipeline Diagrams
6
1
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
lw $t0, 4($s0) |  |  | F* | F* | F | = |  |  |  |  |  |  |  |  |  | 
lw $s0, 0($s0) |  |  |  |  |  | F | D | X | M | W |  |  |  |  |  | 
bne $s0, $zero, LOOP |  |  |  |  |  |  | F | D* | D* | D | X | M | W |  |  | 
lw $t0, 4($s0) |  |  |  |  |  |  |  | F* | F* | F | D | X | M | W |  | 
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)

## Slide 46: Pipeline Diagrams
6
2
insn\cycle | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
lw $s0, 0($s0) | F | D | X | M | W |  |  |  |  |  |  |  |  |  |  | 
bne $s0, $zero, LOOP |  | F | D* | D* | D | X | M | W |  |  |  |  |  |  |  | 
lw $t0, 4($s0) |  |  | F* | F* | F | = |  |  |  |  |  |  |  |  |  | 
lw $s0, 0($s0) |  |  |  |  |  | F | D | X | M | W |  |  |  |  |  | 
bne $s0, $zero, LOOP |  |  |  |  |  |  | F | D* | D* | D | X | M | W |  |  | 
lw $t0, 4($s0) |  |  |  |  |  |  |  | F* | F* | F | D | X | M | W |  | 
sw $s1, 0($t0) |  |  |  |  |  |  |  |  |  |  | F | D* | D | X | M | W
Assume forwarding and bypassing with MEM-to-MEM. Employ predict-not-taken policy and resolve branches in ID (with EX forwarding). Complete the pipeline diagram.
LOOP:
lw $s0, 0($s0)
bne $s0, $zero, LOOP # taken then not taken lw $t0, 4($s0)
sw $s1, 0($t0)